## Slide 1: ICAS: Integrated Circuit Attack Surface an Extensible Framework for Estimating the Susceptibility of IC Layouts to Additive Trojans Timothy Trippel1, Kang G. Shin1, Kevin B. Bush2, & Matthew Hicks3
1 University of Michigan
2 MIT Lincoln Laboratory
3 Virginia Tech

## Slide 2: Hardware is the Foundation!
Hardware flaws weaken even
formally verified software.
Applications
Operating System
Hypervisor
Firmware
Hardware

## Slide 3: State of Systems Security
Applications
Operating System
Hypervisor
Firmware
Hardware
Software security community has developed mechanisms to both identify and prevent vulnerabilities/attacks
Attackers are forced to lower levels  hardware
Economic forces make developing secure hardware challenging
Fuzzing
KASLR
Secure Boot
DEP
ASLR
Symbolic Execution
TXT

## Slide 4: Hardware Development Process
RTL Design
(Behavioral)
Synthesis
(Structural)
Place-&-Route
(Physical)
Fabrication
Packaging
3rd Party IP
Verification
Verification
Verification
Verification
$$$
$
$$
$$
$$$$
$$$
HDL
HDL
GDSII
Silicon Die
HDL

## Slide 5: Outsourcing Reduces Trust
RTL Design
(Behavioral)
Synthesis
(Structural)
Place-&-Route
(Physical)
Fabrication
Packaging
3rd Party IP
Verification
Verification
Verification
Verification
$$$
$
$$
$$
$$$$
$$$
= Trusted
= Untrusted
HDL
HDL
GDSII
Silicon Die
HDL
How do we know our designs won’t be modified to include a backdoor, or a hardware Trojan?

## Slide 6: Hardware Flaws
Bugs
Trojans
Hardware
Foothold
Unintentional
Intentional
Parametric [Kumar et al.]
A2 [Yang et al.]
TSCs [Lin et al.]
KPTI
PTE Inversion, L1D Flush
Retpoline, IBRS, STIBP, IBPB

## Slide 7: Untrusted Foundry Defenses
1. Visual Inspection
2. Side-Channel
3. Functional Testing
Fabrication
Prevention
Detection
Scalability
Logic Locking
Split Manufacturing
Small Trojans
Complex Triggers
Layout Filling
SAT Attacks
Proximity Attacks
Small Trojans
Kerckhoffs’s 2nd Principle

## Slide 8: Problem
Should we care about the threat of hardware Trojans?
Why are current preventative defenses ineffective?

## Slide 9: Solution
We NEED insight!
  What makes a circuit layout amenable to attack?
  Why are preventative defenses inadequate?
How are IC layouts constructed?
How does one insert a Trojan into a layout?
ICAS: IC Attack Surface

## Slide 10: Integrated Circuit Construction
Top View
Side View
Silicon Wafer
Circuit Die
Device Layer
Dielectric
Dielectric
Metal Layer
Metal Layer
Intel 14nm Broadwell Metal Layers
Photo from: https://www.extremetech.com/computing/193200-intels-14nm-
broadwell-chip-reverse-engineered-reveals-impressive-finfets-13-layer-design
Device Layer Floorplan
a
a
a
a
45nm Intel Xeon X7550
Photo from: https://hardforum.com/
threads/intel-xeon-processor-x7550-hi-res-macro-of-cpu.1969063/
Photo from: https://www.extremetech.com/computing/
277870-intel-issues-update-on-supply-problems-at-14nm
Density: 60-80%

## Slide 11: How are Hardware Trojans Inserted?
2. Trojan/Victim Integration
Locate unblocked security-critical wire to connect Trojan to/near.
3. Intra-Trojan Routing
Route Trojan Trigger/Payload
to integration point.
Type | Size (# additional gates/wires) | Stealth | Controllability
Additive | > 0 | High | High
Substitution | 0 | Medium | Low
Subtractive | < 0 | Medium | Low
1. Trojan Placement
Locate empty placement sites on the device layer for Trojan components.
Trigger-Space
Net Blockage
Route Distance
Device Layer
Dielectric
Dielectric
Metal Layer
Metal Layer
a
aå

## Slide 12: ICAS: Integrated Circuit Attack Surface
ICAS estimates the susceptibility of an IC layout to Additive Trojan insertion
  Nemo – helps identify nets that influence security-critical nets
  GDS2-Score – computes metrics
    Trigger-Space  Trojan Placement
    Net-Blockage  Victim/Trojan Integration
    Route-Distance  Intra-Trojan Routing
Fabrication
Physical Layout
ICAS
Nemo
GDS2-Score
Security Metrics
Netlist
GDSII
Front-End
Design
Front-End
Design

## Slide 13: ICAS Metrics
Trigger-Space
Net Blockage
Route Distance
= Security-Critical Wire
= Unused Placement/Routing Resources
OR1200 Processor
a
Unblocked
&

Attack Surface

## Slide 14: Justification for Metrics
Encapsulates the majority of additive hardware Trojans demonstrated
  Add Transistors
  Add Wires
  Add Both
Metrics are flexible and can be interpreted:
  Individually
  Comprehensively
Additive (Layout-Level) Trojans
Design Type?
Add Transistors?
Parasitic Wire
RD
Parasitic Circuit
TS, RD
Short-Circuit
NB, RD
Functional
TS, NB, RD
Standalone
Yes
No
Integrated
Yes
No
TS = Trigger Space; NB = Net Blockage; RD = Route Distance
Add Transistors?

## Slide 15: Evaluation
Uncover the effectiveness of existing layout-level defenses
  Undirected
  Directed
Demonstrate ICAS metrics show where IC layouts are most vulnerable to specific attacks
Study 60+ IC layouts
  Three open-source cores:
    OR1200 Processor
    AES Accelerator
    DSP Accelerator
  IBM 45nm FDSOI process
  Cadence Genus – Synthesis
  Cadence Innovus – Layout
OR1200
AES
DSP
supv
key
next_out

## Slide 16: Preventive Layout-Level Defenses
Undirected – tune layout parameters to probabilistically constrict placement & routing resource utilization [Xiao et al HOST’13]
Directed – constrict resource utilization around security-critical wires [Ba et al. ISVLSI’16]
Trojan Designs | # Gates | # Placement Sites | Timing Critical? (Route Distance Constrained?)
A2 Analog [Yang et al. S&P’16] | 2 | 20 | No
A2 Digital [Yang et al. S&P’16] | 91 | 1444 | Yes
Privilege Escalation [Hicks et al. S&P’10] | 25 | 342 | Yes
Key Leak [Salmani et al. ICCD’13] | 187 | 2553 | Yes
Hardware Trojans from the Literature

## Slide 17: Attack Surface with Undirected Defense
Undirected Layout Defenses
  Constrict placement resources
    Core density [Xiao et al. HOST’13]
  Constrict routing resources
    Maximum transition time
Deployed on OR1200 only
Route Distance plot shows Attack Surface
  Each heatmap represents an IC layout
  Each heatmap column is a histogram
  Each color-coded rectangle indicates the resources required to implement an attack
Thousands of attack configurations still possible!
*Clock frequency held at 1 GHz across all layouts

## Slide 18: Attack Surface with Directed Defense
Directed Layout Defense
  Constricting resources nearest security-critical wires
  Directed layout filling defense (up to 95% total density)
Deployed on all designs with the same layout parameters across each
Route Distance Plot shows Attack Surface
Thousands of attack configurations still possible!
[Ba et al. ISVLSI’16]

## Slide 19: Conclusion
Modern IC layouts leave a plethora of placement/routing resources for foundry-side attackers to exploit
Preventative defenses against foundry-level attacks are placement focused and inadequate against small Trojans, like A2
What about routing centric defenses?
ICAS aim to make security a first-class concern alongside power, performance, & area

## Slide 20: Questions?
trippel@umich.edu
https://timothytrippel.com
ICAS Repositories:
https://github.com/mit-ll/nemo
https://github.com/mit-ll/gds2-score
DISTRIBUTION STATEMENT A. Approved for public release. Distribution is unlimited. This material is based upon work supported by the Under Secretary of Defense for Research and Engineering under Air Force Contract No. FA8702-15-D-0001. Any opinions, findings, conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the Under Secretary of Defense for Research and Engineering.
This material is based upon work supported by the National Science Foundation Graduate Research Fellowship Program under Grant No. DGE 1256260. Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation.