## Slide 1: WALNUT: Waging Doubt on the Integrity MEMS Accelerometers with Acoustic Injection Attacks
Timothy Trippel, Ofir Weisse, Wenyuan Xu, Peter Honeyman, Kevin Fu

## Slide 2: Sensors Drive Autonomous Systems
Should we trust sensors?
Notes: Sensors are devices that measure environmental stimuli and are deployed in …

## Slide 3: Consider an Adversary?
Notes: Imagine the following scenario... you are riding along in your car that uses a MEMS accelerometer sensor to autonomously deploy the airbags.
An adversary has taken control of the car's entertainment system and is playing strange acoustic tones.
It turns out...
.................
The main questions I addressed in this research were:
Can an adversary control the output of a sensor (specifically MEMS accelerometers) and modify the behavior of an autonomous system?
What can we do to ensure the safety and integrity of cyber-physical systems?

## Slide 4: Overview
Spoofing MEMS accelerometers acoustics
Controlling an accelerometer’s output
Infiltrating an autonomous system via its sensors
Defending accelerometers from acoustic attacks

## Slide 5: MEMS Sensors
Micro-Electro-Mechanical Systems
  Accelerometers
  Gyroscopes
  Etc.
Advantages:
  Low Cost – easy to manufacture
  Low Power – some < 1 mA
  Small Size – integrated circuit
*Photos courtesy of “MEMS Accelerometers – Seminar”, by Matej Andrejašič.
IC Package
MEMS Accelerometer*

## Slide 6: How Acoustics Spoof MEMS Accelerometers

## Slide 7: Acoustics Affect Accelerometers
Variable
Capacitor
+ + + + + + + + + +
+
-
-
-
-
-
-
-
-
Sensing
Mass
-
MEMS Component
Capacitance  Voltage
Variable
Capacitor
+ + + + + + + + + +
+
-
-
-
-
-
-
-
-
Sensing
Mass
-
MEMS Component
d(t)
Acceleration = s(t)
A1sa(t)
ŝ(t) = s(t) + A1sa(t)
s(t)
∆Capacitance
Resonant Frequency
1. Signal Generation
Sensing
Mass
Capacitance
Voltage
Amplifier
LPF
ADC
2. Signal Processing

## Slide 8: How Common is this Vulnerability?
40 Accelerometers
  20 Models
  5 Manufacturers
Frequency Sweep
  0 – 30 kHz
  50 Hz Interval
  256 Samples
    Standard Deviation
    Mean
Mechanically
Decoupled
Acoustic Isolation Chamber
Sound
Amplifier
Function Generator
5 kHz
Accelerometer
Notes: We looked at a sufficient number of devices to notice some are and some are NOT vulnerable
1. What is the Resonant Frequency?
2. How does False Acceleration Manifest Itself?

## Slide 9
Standard Deviation
Mean Shift
Output Biasing Attack
Output Control Attack
1. Fluctuating
2. Constant

## Slide 10: Controlling the Output of an Accelerometer

## Slide 11: Output Biasing: (1) Stabilize Spoofed Measurements
ADC
Analog Accel. Signal
Digital Accel. Signal
Nyquist

## Slide 12
……….
t
t

## Slide 13: Output Biasing: (2) Shape Desired Output Signal
Desired Accelerometer
Output Signal
MEMS Resonant Frequency
(Carrier Signal)
Modulated Acoustic
Attack Signal
=
+

## Slide 14
W
A
L
N
U
T
W
A
L
N
U
T

## Slide 15: Altering System Behavior through its Accelerometer

## Slide 16: Samsung Galaxy S5
Smartphone is ideal target  speaker and accelerometer COLOCATED!
Phone application uses accelerometer to maneuver an RC car
  Application: iSpy Toys
  Accelerometer: MPU6500
1g = Backward
0.3g = Stop
0g = Forward
Orientation of Phone X-axis vs. Car Actions
X-axis
X-axis
X-axis
RC Car
Car Commands
Spoof Phone Orientation with Acoustics!
Notes: ****Proof of Concept****

## Slide 17: Samsung Galaxy S5
RC Car
Samsung Galaxy S5
Car Commands
Accelerometer Readings

## Slide 18: Samsung Galaxy S5

## Slide 19: Defending Accelerometers Against Acoustic Attacks

## Slide 20: Defending Against the Adversary
Hardware
Software
Prevent
Increase Difficulty
Increase Difficulty
Prevent
Increase Difficulty
Increase Difficulty
No Benefit
No Benefit
Notes: Low-Cost Software Filtering

## Slide 21: Randomized Sampling
Destroy predictability of sampling regime
Add random delay (w.r.t. Fres) to beginning of each sampling interval
Randomized Sampling
Step 1: Stabilize Spoofed Measurements
……….
t
t
t
……….
t+r1
t+r2
t+rn
Notes: What do we know?
  Accelerometers can only be spoofed at its resonant frequency
  Resonant frequencies are known at design time
Fs = 2550 Hz  ~ 0.4ms
Fres = 5100 Hz  ~ 0.2ms

## Slide 22: Randomized Sampling

## Slide 23: Conclusions
Found 85% MEMS accelerometers models affected by acoustics
Spoofed sensor data can be controlled by an adversary
Adversaries can control autonomous systems
Demonstrated how to mitigate acoustic attacks on MEMS accelerometers
Need to have security in mind when designing sensor hardware

## Slide 24: Questions?
Tim Trippel
trippel@umich.edu
For demo videos please visit: https://spqr.umich.eecs.edu/walnut

## Slide 25: Coordinated Disclosure
Notified all affected semiconductor manufactures
  Analog Devices
  Bosch PSIRT
  InvenSense
  STMicroelectronics
  Murata
Notified U.S. Department of Homeland Security ICS-CERT to coordinate disclosure with affected device manufactures
Notified device manufactures
  Fitbit
  Samsung
See project website for more details (https://spqr.eecs.umich.edu/walnut)